## Slide 1: 地球低軌道環境観測衛星「てんこう」，および「てんこう２」
Microsatellite utilization symposium
January 18th, 2022
日本大学 理工学部 航空宇宙工学科
奥山 圭一

## Slide 2
Deep Space Communication Experiment Probe “Shin-en 2”
Low Earth Orbit Environment Observation Satellite "Ten-Koh”
In order to complete the development in about 15 months, Shin-en 2 heritage was applied.
“Shin-en 2” and “Ten-Koh”

## Slide 3
Launching: December 3rd, 2014
Size: 470 x 495 x 495 mm
Weight: 17.8 Kg
A Piggyback Probe for The JAXA’s Asteroid Explorer “Hayabusa 2”

## Slide 4
“Hayabusa 2” and “Shin-en 2”

## Slide 5
Orbits of the Earth and “Shin-en 2”

## Slide 6
External structure of "Shin-en 2"
Structure made of carbon fiber reinforced thermoplastic resin composite material “CFRTP”

## Slide 7: Data reception result from “Shin-en 2”

## Slide 8
出典： http://spaceweather.com/
出典： http://cosmology.com/ClimateChange104.html

## Slide 9
出典：太陽風と地球磁場（別冊サイエンス）
出典： http://www.env01.net/fromadmin/contents/2015/2015_09.html

## Slide 10
出典： http://www.env01.net/fromadmin/contents/2015/2015_09.html

## Slide 11
CFRTP degradation observation device
Carbon fiber reinforced thermosetting resin composite (CFRP)
Low Earth Orbit Environment Observation Satellite "Ten-Koh”

## Slide 12
CFRTP degradation observation device
Magnetometer
Double Langmuir probe
Ultra low power deep space
communication antenna
Low Earth Orbit Environment Observation Satellite "Ten-Koh”

## Slide 13
Low Earth Orbit Environment Observation Satellite "Ten-Koh”
CFRTP degradition observation device

## Slide 14
Low Earth Orbit Environment Observation Satellite "Ten-Koh”

## Slide 15
Launch environment testing
Rocket environment (launching)
Separation from main vehicle
Space environment testing
20 – 25% of anomalies caused by the space environment (Koga 2016)
Outgassing
UV & X-Ray
SEP
Thermal cycling
Atomic oxygen
Trapped electron & proton flux
Magnetic field
lines
Charge & discharge
Galactic Cosmic Rays
Debris, meteoroid
Testing for survivability
Emerging technologies have bigger susceptibility of failure due to space environment
Low Earth Orbit Environment Observation Satellite "Ten-Koh”

## Slide 16
Mass: 23.3 kg
Shape: Quasi-sphere ~50cm (CFRP)
Orbit: Sun-synchronous, 610 km, 97.8 deg
Launch date: 29 Oct 2018 (Tanegashima, Japan)
Launch vehicle: H-2A (as a piggyback payload)
Development time: 16 months
Main missions:
Investigate the change of physical properties of LATS and CFRP materials exposed to the space environment.
To detect MeV-range electrons in LEO and investigate the space radiation environment in the presence of a low solar activity.
To characterize the plasma environment around a spinning spacecraft.
LATS: Lightweight Ablator series for Transfer vehicle
CFRP: Carbon Fiber Reinforced Polymer
Low Earth Orbit Environment Observation Satellite "Ten-Koh”

## Slide 17
Ten-Koh satellite
Magnetometer
GNSS antenna
Material Mission (material samples board)
GNSS antenna
Material Mission (material samples board)
Monopole antennas
Monopole antennas
Magnetometer
Monopole antennas
DLP probes (electrodes)
Solar panels
AS

## Slide 18
Ten-Koh satellite
DLP measurement electronics
CPD
(CMOS detectors)
CPD
(Liulin detector)
DLP measurement electronics
ECU (Experiment Control Unit)
WJST TxRx
DLP isolated power & GND
RDS_PL
RDS_BUS
Battery 1
RDS_PL
RDS_PL
Low Earth Orbit Environment Observation Satellite "Ten-Koh”

## Slide 19
Ten-Koh CPD payload
X-rays detectors range:
47kV to 680 kV
Power and data interface
CMOS-1
CMOS-0
SIDE A
SIDE D
SIDE C
SIDE B
CMOS-2
CMOS-3
CMOS-4
CMOS-5
CMOS-6
CMOS-7
Liulin spectrometer
CPD CMOS & Liulin detectors distribution
Sensor Functionality
CMOS-0: X-Ray
CMOS-1: Polyethylene Sphere (shielding experiment)
CMOS-2: Open for ambient radiation measurements
CMOS-3: Polyethylene Sphere (shielding experiment)
CMOS-4: Open for ambient radiation measurements
CMOS-5: Polystyrene Sphere (tissue equivalent)
CMOS-6: X-Ray
CMOS-7: Polystyrene Sphere (tissue equivalent)
Liulin: Dosimeter (spectrometer)
Low Earth Orbit Environment Observation Satellite "Ten-Koh”

## Slide 20
In-orbit testing strategy: Liulin detector
Parameter | Min | Max
Dose rate [Gy/h] | 1.12x10-8 | 0.188
Flux [particles/cm2/s] | 0.01 | 10000
Deposited energy range [MeV] | 0.081 | 20.833
Energy resolution [MeV/ch] | 0.0814 | 
Total number of channels | 256 | 
Si detector (2 x 1 cm)
Low Earth Orbit Environment Observation Satellite "Ten-Koh”

## Slide 21
Particle identification based on the dose-to-flux ratio (D/F)
Low Earth Orbit Environment Observation Satellite "Ten-Koh”

## Slide 22
Predicting TID
AE-8: 1.824610-7 Gy
CRRESELE: 9.8427910-7 Gy
DOSE
AP-8: 2.433810-6 Gy
CRRESPRO: 6.607110-6 Gy
CREME96: 7.6869610-10 Gy
(Z1 to Z10)
TIDAE-8,AP-8,CREME96 = 2.61710-6 Gy
TIDCRRESELE,CRRESPRO,CREME96 = 7.59210-6 Gy
Low Earth Orbit Environment Observation Satellite "Ten-Koh”

## Slide 23
SEU events source
rprotons = 0.9184
rGCR = -0.2205
Correlation coefficient
Low Earth Orbit Environment Observation Satellite "Ten-Koh”

## Slide 24
24
Low Earth Orbit Environment Observation Satellite "Ten-Koh”

## Slide 25
25
25
Low Earth Orbit Environment Observation Satellite "Ten-Koh”

## Slide 26
The Low Earth Orbit space environment observation satellite Ten-Koh 2
Second version of Ten-Koh with upgraded experiments.
Launch: FY2022.
Mass: 10 kg
Orbit: TBD (~51 degree inclination at 500 km)
Vehicle: H-3 rocket and first HTV-X vehicle
Shape and size: 6U CubeSat
Technology demonstration satellite in LEO
26
26
26
26

## Slide 27
The Low Earth Orbit space environment observation satellite Ten-Koh 2
27
27
27

## Slide 28
The Low Earth Orbit space environment observation satellite Ten-Koh 2
28
28
28

## Slide 29
Observation of the global environment using a high-resolution camera
Geospace observation using a high-energy charged particle detector
Observation of space environment resistance of advanced space materials
Continuous operation of linear transponders
High-speed data transmission test (4FSK 19.2k BPS)
C band (5.8GHz band) communication technology demonstration
The Low Earth Orbit space environment observation satellite Ten-Koh 2
29
29
29
29

## Slide 30
And to our lunar orbiter mission
30
30
30
30